# TECHNICAL DATA SHEET

510 Series

“Premium”

Roof Coat Semi Gloss

Silicone/Acrylic

FIVE YEAR WARRANTY

Specially formulated for the Florida climate

__________________________________________________________________________________________

Povia 510 Silicone/Acrylic Premium Roof Coat Semi Gloss is a blend of the finest acrylic resins and pigments available.  Povia 510 is a premium quality, acrylic roof coating designed for maximum performance against Florida’s extreme weather conditions.  Povia 510 is modified with a silicone additive to provide superior water resistance and long term durability.  Povia 510 also provides maximum mildew resistance and UV protection.  Povia 510 has the acrylic advantages of durability, adhesion and flexibility.

__________________________________________________________________________________________

RECOMMENDED USES:

For properly primed masonry, metal, shingle and aggregate roofs.  Not recommended for flat roofs.

SURFACE PREPARATION:

Dirt, grease, grime and any foreign material must be removed before application of new coating.  Insure surface is clean and dry.  Contact a Povia Paints representative for detailed surface preparation specifications.

APPLICATION:

Mix product thoroughly.  Apply with brush roller or airless spray. Apply when surface temperatures are at least 50 deg. and rising.  Do not thin with paint thinners.

RECOMMENDED THINNER:

Povia 510 does not require thinning and should be used as is, directly from the container.

RECOMMENDED PRIMER

Contact a Povia Paints representative for specific priming information.

TECHNICAL DATA:

Finish: Semi-Gloss

Pigment Type: Titanium Dioxide

Vehicle Type: Acrylic Copolymer

Solvent Type: Water

% Solids By Weight: 50% +/- 2%

% Solids By Volume: 38% +/- 2%

Density: 10.45 lbs. Per gallon

Viscosity @ 75 deg. F (24 deg. C): 105 +/- 2 K.U.

Coating VOC: <150 g/l

Estimated Dry Time:  To touch 30-60 minutes ; Recoat 4-6 hours

Flash Point, Minimum: Not Flammable

Flame Spread: Class A rating on non-combustible substratum

Recommended Dry Film Thickness Per Coat: 1.5-2.5 Mils DFT.

Clean Up: Clean up drips and spills immediately using a damp cloth.  Clean tools and equipment with soap and fresh water.

Coverage (Theoretical): Coverage will depend on porosity and contour of the surface being coated.    Coverage typically averages 200-300 square feet per gallon.

Povia 510  is water based.  Do not Freeze.

CAUTION: KEEP OUT OF REACH OF CHILDREN!

WARNING! If you scrape, sand or remove old paint, you may release lead dust.  LEAD IS TOXIC.  EXPOSURE CAN CAUSE SERIOUS ILLNESS, SUCH AS BRAIN DAMAGE, ESPECIALLY IN CHILDREN.  PREGNANT WOMEN SHOULD ALSO AVOID EXPOSURE.  Wear an NIOSH-approved respirator to control lead exposure.  Carefully clean up with a HEPA vacuum and a wet mop.  Before you start, find out how to protect yourself and your family by contacting the National Lead Information Hotline at 1-800-424-LEAD or log on to www.epa.gov/lead.

Technical data contained herein is true and accurate at the date of issue, but is subject to change without notice.  A Povia Paints representative should be contacted with any questions concerning product information or application procedures.  Our products conform to Povia quality standards, but no other warranty is expressed or implied.  Liability, if any, is limited to the replacement of product or purchase price.

## Povia Paints, Inc., 5601 Banner Dr., Ft. Myers, FL 33912  239-791-0011